How to Update the Firmware

Update the PROM code:

- Modify the configure file for PROM code updating

Specify the directory path and image file name for PROM code.

- Enable your TFTP server.

- Enter console program; select Firmware and Configuration Update in the main menu.

- Set the Software Update Mode to “Network”.

- Specify the IP address of your TFTP server.

- Set Use Config Files to “Enable”

- In File Name field, specify the path and file name of config file. The following screen appears:

- Press REBOOT TO START UPDATE to initiate the update sequence.

- Restart the switch. Check the version of PROM code. is it the correct version you want to update?

Update the RUNTIME code:

- Modify the configure file for RunTime code updating

Specify the directory path and image file name for RunTime code.

- Enable your TFTP server.

- Enter console program; select Restart System in the main menu.

- Enter Power On Self-Test screen; the following screen appears:

- When you see * Testing Switch Hardware: PROM Code Checksum(Image 1)  ….PASSED, please press Ctrl-C keys to enter BOOT MENU. The follow screen appears:

- Please select Configure  IP to assign an IP address to the switch. Note that press Ctrl-S keys to save the IP setting.

- Enter BOOT MENU; select Update Firmware and Configuration Files in the main menu.

- Set the Software Update Mode to “Network”.

- Specify the IP address of your TFTP server.

- Set Use Config Files to “Enable”

- In File Name field, specify the path and file name of config file. The following screen appears:

- Press RESET SWITCH TO START UPDATE to initiate the update sequence.

- Restart the switch. Check the version of PROM code. is it the correct version you want to update?

# Text boxes

#Code_type=PROM

#Image_file="e:\switch\dgs3208\3208Prom.tfp"

Code_type=RUNTIME

Image_file="e:\switch\dgs3208\dgs3208.tfp"

#Code_type=CONFIG

#Image_file="g:\d-link\des-32~1\basic_25.bc"

# specify IP address

#Ip_addr = 10.41.52.35

# specify subnet mask

#Subnet_mask = 255.0.0.0

# specify default gateway

#Default_gateway = 10.254.254.254

Code_type=PROM

Image_file="e:\switch\dgs3208\3208Prom.tfp"

#Code_type=RUNTIME

#Image_file="e:\switch\dgs3208\dgs3208.tfp"

#Code_type=CONFIG

#Image_file="g:\d-link\des-32~1\basic_25.bc"

# specify IP address

#Ip_addr = 10.41.52.35

# specify subnet mask

#Subnet_mask = 255.0.0.0

# specify default gateway

#Default_gateway = 10.254.254.254